## Slide 1: Operating systems
Simple OS: an operating system for the NXP K70 Tower System

## Slide 2: TABLE OF CONTENTS 01 shell REPL Available Commands Date & Time 02 Devices & I/O Devices Implemented SVC Interrupts 03 Multitasking Processes and PCB spawn, wait, kill 04 FiNAL PROJECT Summary Implementation

## Slide 3: -Donald Knuth “Premature optimization is the root of all evil”

## Slide 4: SHELL 01
After this, there is no turning back. Take the blue pill - you wake up in your bed and believe whatever. Take the red pill - I show you how deep the rabbit-hole goes.
-MORPHEUS

## Slide 5: Shell features available commands -Core Commands: echo, date, exit, help, malloc, free, memorymap, memset, memchk, fopen, fclose, fgetc, fputc, create, delete, ls, touch2led, pot2ser, therm2ser, pb2led, catfile, cat2file, flashled, spawn, kill, multitask, ps -Addl Commands: malfree, fgets, fputs, seek, uartsendmsg, busywait repl -Core functionality: Console REPL loop utilizes the K70’s UART2 port for STDIN, STDOUT and STDERR - Shell support for quotation marks and escape characters date/time -Core functionality: 1ms-accurate date/time can be set and retrieved from command line -Shell automatically acquires current date and time at compile time -Supports simplified ISO 8601 date/time string

## Slide 6: DEVICES & I/O 02
“What we've got here is failure to communicate.”
-THE CAPTAIN

## Slide 7: DEVICE LAYER STREAMS AND FILES - struct streams - file descriptors -device-independent IO implementation DEVICES SUPPORTED - UART -SDHC FAT32 -TWR-LCD-RGB -DAC/ADC -Touch Sensors -LEDs -Timers FAT32 -Core Functionality: ls, create, delete, reading and writing files -Addl Functionality: ls supports extended directory listing, last modification date/time, creation date/time, last access date

## Slide 8: MULTITASKING 03
“When we think we're multitasking we're actually multiswitching. We think we're being productive. We are, indeed, being busy. But in reality we're simply giving ourselves extra work.”
-MICHAEL HARRIS

## Slide 9: Multitasking processes and the pcb shell commands
-PCB structs
-Round robin scheduler
-spawn
-wait
-kill
-multitask

## Slide 10: FINAL PROJECT 04
We meet again, at last. The circle is now complete. When I left you I was but the learner. Now, *I* am the master.
-DARTH VADER

## Slide 11: Dac synthesizer
A/V final project combines new device-independent I/O, basic electronics, and continuous PDB timer
cmd_synth implements a synthesizer with two waveforms and a functioning ASR envelope

## Slide 12: implementation details
shell
Validates user input and places OS requests
Hardware
Voltage outputs over DC as subdivisions of reference voltage
AC conversion at hardware level
Device
16-step DAC buffer continuously triggered by PCB
i/o
Further validates input and initializes device

## Slide 13: statistics (as of 5/14)
github commits
361
sloc
~7500
(not including the K70 header file and comments)
Shell Cmds
35
devices
18

## Slide 14: Operating systems
Ben Feuer
www.benfeuer.com